## Slide 1
AeroNavX
Autonomous Drone Design,
Navigation & AI Vision System
Unlox Drone Engineering Program | April 2026
ArduPilot SITL · DroneKit-Python · OpenCV · Linux Mint 22

## Slide 2
PROJECT OVERVIEW
8
Project Modules
3
Python Scripts
4
Flight Logs
15
PPT Slides
What is AeroNavX?
AeroNavX is a fully autonomous quadcopter simulation system covering the complete UAV engineering stack — from mechanical design and power systems to autonomous Python programming and AI computer vision. Built and tested on ArduPilot SITL on Linux Mint 22.
Simulation Platform: ArduPilot SITL | Language: Python 3.12 | OS: Linux Mint 22 (Ubuntu 24.04)

## Slide 3
OBJECTIVES & PROBLEM STATEMENT
Problem
AeroNavX Solution
✗ Frame design optimization
✓ 450mm X-frame CAD in Fusion 360
✗ Power system configuration
✓ 2.34:1 TWR with EMAX 2216 + 4S LiPo
✗ Real-time sensor noise
✓ EKF3 filter + IMU calibration
✗ Unstable autonomous navigation
✓ DroneKit waypoint mission scripts
✗ Inaccurate landing
✓ Vision-based OpenCV landing system
✗ Lack of obstacle awareness
✓ Real-time OpenCV obstacle detection

## Slide 4
MODULE 1 — DRONE FRAME DESIGN (CAD)
Frame Type
X-Quadcopter Config
Motor-to-Motor
450mm diagonal
Arm Material
Carbon fiber composite
Center Plate
PCB fiberglass
Propeller Clearance
15mm minimum
Landing Gear
60mm clearance
Center of Gravity
Geometric center ±5mm
Total Frame Weight
282g
Design Highlights
• X-config for stable autonomous flight
• Carbon arms reduce vibration to IMU
• Pixhawk mounted on anti-vibration pads
• PDB integrated into bottom plate
• Camera mount on forward arm
• Compatible with 10" propellers

## Slide 5
MODULE 2 — POWER & PROPULSION SYSTEM
MOTORS
EMAX 2216 KV880
850g thrust each · 22A max
ESCs
Hobbywing XRotor 30A
OPTO · 2S-4S · PWM
PROPS
APC 10×4.5 GFN
10" dia · 4.5" pitch · CW+CCW
BATTERY
Tattu 4S 5200mAh 45C
14.8V · 380g · XT60
Key Calculations
Total Thrust: 4 × 850g = 3,400g
All-Up Weight (AUW): 1,450g
Thrust-to-Weight Ratio: 3400 / 1450 = 2.34 : 1 ✓
Hover Throttle: ~42.6% (efficient)
Avg Current (mission): ~18A
Estimated Flight Time: ~13.9 minutes

## Slide 6
MODULE 3 — FLIGHT CONTROLLER & SENSOR SETUP
Hardware Stack
Flight Controller
Pixhawk 2.4.8
Firmware
ArduCopter 4.x
GPS
u-blox M8N w/ compass
IMU
Triple redundant (ICM/MPU/LSM)
Barometer
MS5611 (temp compensated)
GCS Software
QGroundControl / Mission Planner
Calibrations Performed
✓ Accelerometer (6-position)
✓ Compass (live onboard)
✓ Radio (endpoints + trim)
✓ ESC (all 4 synchronized)
✓ Level calibration / hover trim
✓ Geo-fence parameter upload

## Slide 7
MODULE 4 — AUTONOMOUS FLIGHT PROGRAMMING (DroneKit)
# Connect to SITL simulator vehicle = connect('127.0.0.1:14550', wait_ready=True) def arm_and_takeoff(target_alt): vehicle.mode = VehicleMode("GUIDED") vehicle.armed = True vehicle.simple_takeoff(target_alt) # Navigate 4 waypoints for wp in waypoints: vehicle.simple_goto(wp)
time.sleep(
10) # Return to Launch vehicle.mode = VehicleMode("RTL")
Mission Results
✓ Connected
SITL on 127.0.0.1:14550
✓ Armed
GUIDED mode confirmed
✓ Takeoff
Reached 19.5m (target 20m)
✓ WP 1-4
All visited in sequence
✓ RTL
Auto-return + land
✓ Logged
4× .BIN flight logs

## Slide 8
MODULE 5 — OBSTACLE DETECTION & AVOIDANCE (OpenCV)
Processing Pipeline
Camera
Capture
→
BGR → HSV
Conversion
→
Color Mask
Filtering
→
Contour
Detection
→
Area
Threshold
→
Avoidance
Action
Obstacle Types Detected
• Red obstacles (HSV 0-10, 120-255, 70-255)
• Walls and large surfaces
• Markers and colored objects
• Min detection area: 500 px²
Avoidance Maneuvers
Stop: Halt forward motion immediately
Lateral: Move sideways to clear obstacle
Climb: Increase altitude above obstacle
Test Result: Obstacle successfully detected via webcam feed with bounding box drawn and avoidance action printed in real-time

## Slide 9
MODULE 6 — VISION-BASED LANDING SYSTEM (AI/CV)
Landing Algorithm Flow
1
Capture camera frame
2
Convert to HSV color space
3
Mask for green landing pad
4
Find largest contour
5
Calculate pad centroid (cx, cy)
6
Compute alignment error
error_x = cx - frame_w/2
error_y = cy - frame_h/2
7
If |error| < 20px → LAND
Else → correct position
Live Test Results
Landing pad detected
via live webcam feed
Error X:
-285 to -298 px
Error Y:
70 to 124 px
Direction:
Left + Forward
Detection:
Continuous (30 fps)
Alignment msg:
Adjusting position...
'Vision landing system complete!' ✓

## Slide 10
MODULE 7 — AIRSPACE COMPLIANCE & GEO-FENCING
DGCA (India) Regulations
✓ Max altitude: 120m AGL
✓ Visual Line of Sight required
✓ No-fly within 5km of airports
✓ Daylight operations only
✓ UIN required (drones >250g)
✓ RPC for commercial operations
ArduPilot Geo-Fence Config
FENCE_ENABLE
1 (Active)
FENCE_TYPE
Circle + Altitude
FENCE_ACTION
RTL on breach
FENCE_ALT_MAX
100m
FENCE_RADIUS
150m
RTL_ALT
30m (30,000mm)
Failsafes Active: Battery (RTL @3.5V/cell, Land @3.3V) · RC Loss (RTL) · GPS Loss (AltHold/Land) · Geo-fence breach (RTL)

## Slide 11
MODULE 8 — FINAL INTEGRATED SIMULATION MISSION
01
ARM & TAKEOFF
Climb to 20m
GUIDED mode
→
02
WAYPOINT NAV
4 GPS waypoints
10s per leg
→
03
OBSTACLE DETECT
OpenCV vision
Avoidance trigger
→
04
VISION LAND
Pad detection
Error < 20px
→
05
RTL + LAND
Auto return
Precision land
Flight Log Evidence
Log File:
00000001.BIN – 00000004.BIN (4 sessions)
Format:
ArduPilot Binary Log (MAVLink telemetry)
Contents:
IMU, GPS, altitude, throttle, mode transitions
Tool:
Mission Planner Log Viewer / MAVExplorer

## Slide 12
TECHNOLOGY STACK & DEVELOPMENT ENVIRONMENT
Simulation
• ArduPilot SITL
• MAVProxy Console
• ArduCopter Firmware
Autonomy
• DroneKit-Python
• pymavlink
• MAVLink Protocol
Vision / AI
• OpenCV (cv2)
• NumPy arrays
• HSV color detection
Analysis
• matplotlib
• Python 3.12
• .BIN log files
Hardware
• Pixhawk 2.4.8
• EMAX 2216 KV880
• 4S LiPo Battery
Platform
• Linux Mint 22
• Ubuntu 24.04 base
• Python venv

## Slide 13
CHALLENGES & SOLUTIONS
⚠ DroneKit incompatible with Python 3.12
✓ Patched MutableMapping: used sed to fix collections.abc import in dronekit __init__.py
⚠ 'past' module not found error on import
✓ Installed 'future' package via pip install future
⚠ sim_vehicle.py command not found in PATH
✓ Reloaded .profile with '. ~/.profile' to add ArduPilot tools to PATH
⚠ First ArduCopter build took 45+ minutes
✓ Subsequent launches use cached binary — starts in seconds
⚠ Vision landing detecting false positives
✓ Tuned HSV green range (40-80, 70-255) to reduce ambient light interference

## Slide 14
RESULTS SUMMARY — ALL DELIVERABLES
1
CAD Frame Design
Fusion 360 X-frame 450mm
✓
2
Power & Propulsion Report
Motor, ESC, battery, TWR calc
✓
3
Flight Controller Config
copter.parm ArduPilot
✓
4
DroneKit Mission Code
mission.py — tested on SITL
✓
5
Obstacle Avoidance Code
obstacle_avoidance.py — OpenCV
✓
6
Vision Landing Code
vision_landing.py — pad detection
✓
7
Geo-fence & Compliance
DGCA rules + ArduPilot config
✓
8
Simulation Flight Video
Screen recorded SITL mission
✓
9
Flight Logs
00000001-4.BIN from ArduPilot
✓
10
Final Project Report
Full .docx documentation
✓
11
Final PPT
15 slides — this presentation
✓

## Slide 15
Conclusion &
Learning Outcomes
◆ Aerodynamics & UAV physics
◆ Drone CAD design (Fusion 360)
◆ Power system engineering
◆ Flight control (Pixhawk/ArduPilot)
◆ Python-based drone automation
◆ AI-driven computer vision (OpenCV)
◆ Autonomous navigation logic
◆ Real-world UAV regulatory compliance
AeroNavX — Built from scratch. Flown autonomously. Documented completely.
Unlox Drone Engineering Program | April 2026